## Slide 1: Introduction to RTOS
Presented by
Ch.Lavanya
161FA04358

## Slide 2: Operating system (OS) :
An Operating system (OS) is a piece of software that controls the overall operation of the System. It acts as an interface between hardware and application programs.
In a multiuser system it allows several users to share the CPU time, share the other system resources and also avoids the interference of different users in sharing the resources etc. Hence the OS is also known as a resource manager.
An Operating system (OS) is nothing but a collection of system calls or functions. An OS typically provides multitasking, synchronization, Interrupt and Event Handling, Input/Output, Inter-task Communication, Timers and Clocks and Memory Management.

## Slide 3: REAL TIME SYSTEMS:
Real-time systems are those systems in which the correctness of the system depends not only on the Output, but also on the time at which the results are produced (Time constraints must be strictly followed).
  Real time systems are two types:
(i) Soft real time systems
(ii) Hard real time systems.

## Slide 4
Soft Real Time system is one in which the performance of the system is only degraded but, not destroyed if the timing deadlines are not met.
Ex: Air conditioner, TV remote or music player, Bus reservation, automated teller machine in a bank, Lift, etc.
Hard Real Time system is one in which the failure to meet the time dead lines may lead to a complete catastrophe or damage to the system.
Ex: Air navigation system, Nuclear power plant, Failure of car brakes, Gas leakage system, RADAR operation, etc.

## Slide 5: REAL TIME OPERATING SYSTEM (RTOS):
It is an operating system that supports real-time applications by providing logically correct result within the deadline set by the user. A real time operating system makes the embedded system into a real time embedded system.
A Real-Time Operating System (RTOS) comprises of two components, viz., “Real-Time” and “Operating System”.

## Slide 6: RTOS Classification:
RTOS specifies a known maximum time for each of the operations that it performs. Based upon the degree of tolerance in meeting deadlines, RTOS are classified into following categories
Hard real-time: Degree of tolerance for missed deadlines is negligible. A missed deadline can result in catastrophic failure of the system
Firm real-time: Missing a deadly ne might result in an unacceptable quality reduction but may not lead to failure of the complete system
Soft real-time: Deadlines may be missed occasionally, but system doesn’t fail and also, system quality is acceptable

## Slide 7: RTOS Features:
Multithreading and preemptability.
Thread Priority.
Inter Task Communication & Synchronization.
Priority Inheritance.
Short Latencies.

## Slide 8: Basic functions of RTOS:
Time management:
  A high resolution hardware timer is programmed to interrupt the processor at fixed rate (Time interrupt)
  Each time interrupt is called a system tick (time resolution)
Task management:
  Task creation: create a newTCB
  Task termination: remove the TCB
  Change Priority: modify the TCB
  State-inquiry: read the TCB

## Slide 9
Interrupt handling:
  ISR
Memory management:
  No virtual memory for hard RT tasks, Many embedded RTS do not have memory protection
Exception handling :
  missing deadline, running out of memory, timeouts, deadlocks, divide by zero, etc.
Task synchronization:
  Semaphore, Mutex, Avoid priority inversion
Task scheduling:
  Priorities (HPF), Execution times (SCF), Deadlines (EDF), Arrival times (FIFO)

## Slide 10: Requirements on RTOS
Determinism
  Deterministic system calls
Responsiveness
  Fast process/thread switch
  Fast interrupt response
Support for concurrency and real-time
  Multi-tasking
Real-time
  Synchronization
User control over OS policies
  Mainly scheduling, many priority levels
  Memory support (especially embedded)
Controlled code size