## Slide 1: 8051Micro controller

## Slide 3: Microprocessors:
CPU
General-Purpose Micro-processor
RAM
ROM
I/O Port
Timer
Serial COM Port
Data Bus
Address Bus
General-Purpose Microprocessor System
CPU for Computers
No RAM, ROM, I/O on CPU chip itself
Example：Intel’s x86, Motorola’s 680x0
Many chips on mother’s board
General-purpose microprocessor
Notes: Intel’s x86: 8086,8088,80386,80486, Pentium
Motorola’s 680x0: 68000, 68010, 68020,68030,6040

## Slide 4
RAM
ROM
I/O Port
Timer
Serial COM Port
Microcontroller
CPU
A smaller computer
On-chip RAM, ROM, I/O ports...
Example：Motorola’s 6811, Intel’s 8051, Zilog’s Z8 and PIC 16X
A single chip
Microcontroller :

## Slide 5
Microprocessor
CPU is stand-alone, RAM, ROM, I/O, timer are separate
designer can decide on the amount of ROM, RAM and I/O ports.
expansive
versatility
general-purpose
Microcontroller
CPU, RAM, ROM, I/O and timer are all on a single chip
fix amount of on-chip ROM, RAM, I/O ports
for applications in which cost, power and space are critical
single-purpose
Microprocessor vs. Microcontroller
Notes: versatility 多用途的: any number of applications for PC

## Slide 9: Criteria for choosing micro controller

## Slide 11: 8051

## Slide 14: Pin Description of the 8051
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
40
39
38
37
36
35
34
33
32
31
30
29
28
27
26
25
24
23
22
21
P1.0
P1.1
P1.2
P1.3
P1.4
P1.5
P1.6
P1.7
RST
(RXD)P3.0
(TXD)P3.1
(T0)P3.4
(T1)P3.5
XTAL2
XTAL1
GND
(INT0)P3.2
(INT1)P3.3
(RD)P3.7
(WR)P3.6
Vcc
P0.0(AD0)
P0.1(AD1)
P0.2(AD2)
P0.3(AD3)
P0.4(AD4)
P0.5(AD5)
P0.6(AD6)
P0.7(AD7)
EA/VPP
ALE/PROG
PSEN
P2.7(A15)
P2.6(A14)
P2.5(A13)
P2.4(A12)
P2.3(A11)
P2.2(A10)
P2.1(A9)
P2.0(A8)
8051


## Slide 15: Pins of 8051
Vcc（pin 40）：
  Vcc provides supply voltage to the chip.
  The voltage source is +5V.
GND（pin 20）：ground
XTAL1 and XTAL2（pins 19,18）：
  These 2 pins provide external clock.
  Way 1：using a quartz crystal oscillator
  Way 2：using a TTL oscillator
  Example 4-1 shows the relationship between XTAL and the machine cycle.

## Slide 16: XTAL Connection to 8051
Using a quartz crystal oscillator
We can observe the frequency on the XTAL2 pin.
C2
30pF
C1
30pF
XTAL2
XTAL1
GND

## Slide 17: Machine cycle
the smallest time to accomplish any simple instruction is called machine cycle
Find the machine cycle for
(a) XTAL = 11.0592 MHz
(b) XTAL = 16 MHz.
Solution:
(a) 11.0592 MHz / 12 = 921.6 kHz;
machine cycle = 1 / 921.6 kHz = 1.085 s
(b) 16 MHz / 12 = 1.333 MHz;
machine cycle = 1 / 1.333 MHz = 0.75 s

## Slide 18: Pins of 8051（2/4）
RST（pin 9）：reset
  It is an input pin and is active high（normally low）.
    Upon applying a high pulse to RST, the microcontroller will reset and all values in registers will be lost.

## Slide 19: RESET Value of Some 8051 Registers:
0000
DPTR
07
SP
00
PSW
00
B
00
ACC
0000
PC
Reset Value
Register
RAM are all zero


## Slide 20: Pins of 8051（3/4）
/EA（pin 31）：external access
  The /EA pin is connected to GND to indicate the code is stored externally.
/PSEN（pin 29）：program store enable
  This is an output pin and is connected to the OE pin of the ROM

## Slide 21: Pins of 8051（4/4）
ALE（pin 30）：address latch enable
  It is an output pin and is active high.
  8051 port 0 provides both address and data.
  The ALE pin is used for de-multiplexing the address and data by connecting to the G pin of the 74LS373 latch.
I/O port pins
  The four ports P0, P1, P2, and P3.
  Each port uses 8 pins.
  All I/O pins are bi-directional.

## Slide 22: IMPORTANT PINS (IO Ports)
One of the most useful features of the 8051 is that it contains four I/O ports (P0 - P3)
Port 0 （pins 32-39）：P0（P0.0～P0.7）
  8-bit R/W - General Purpose I/O
  Or acts as a multiplexed low byte address and data bus for external memory design
Port 1 （pins 1-8） ：P1（P1.0～P1.7）
  Only 8-bit R/W - General Purpose I/O
Port 2 （pins 21-28）：P2（P2.0～P2.7）
  8-bit R/W - General Purpose I/O
  Or high byte of the address bus for external memory design
Port 3 （pins 10-17）：P3（P3.0～P3.7）
  General Purpose I/O
  if not using any of the internal peripherals (timers) or external interrupts.
Each port can be used as input or output (bi-direction)

## Slide 23: Port 3 Alternate Functions

## Slide 25: Architecture

## Slide 26: Block Diagram

## Slide 27: Program Counter & Data Pointer
They are both 16 bit registers.
Each is to hold the address of a byte in memory
PC contains the address of the next instruction to be executed.
DPTR is made up of two 8 bit register DPH and DPL;
DPTR contains the address of internal & external code and data that has to be accessed.

## Slide 28: A and B CPU registers
Totally 34 general purpose registers or working registers.
Two of these A and B hold results of many instructions, particularly math and logical operations of 8051 cpu.
The other 32 are in four banks,B0 – B3 of eight registers each.
A(accumulator) is used for addition,subtraction,mul,div,boolean bit manipulation and for data transfers.
But B register can only be used for mul and div operations.

## Slide 29: 8051 Flag bits and the PSW register
PSW Register
CY
AC
F0
RS1
OV
RS0
P
--
CY PSW.7 Carry flag
AC PSW.6 Auxiliary carry flag
-- PSW.5 Available to the user for general purpose
RS1 PSW.4 Register Bank selector bit 1
RS0 PSW.3 Register Bank selector bit 0
OV PSW.2 Overflow flag
-- PSW.1 User define bit
P PSW.0 Parity flag Set/Reset odd/even parity
RS1 RS0 Register Bank Address
0 0 0 00H-07H
0 1 1 08H-0FH
1 0 2 10H-17H
1 1 3 18H-1FH

## Slide 30
RAM memory space allocation in the 8051
7FH
30H
2FH
20H
1FH
17H
10H
0FH
07H
08H
18H
00H
Register Bank 0
(Stack) Register Bank 1
Register Bank 2
Register Bank 3
Bit-Addressable RAM
Scratch pad RAM
Memory Organization

## Slide 31: Stack in the 8051
The register used to access the stack is called SP (stack pointer) register.
The stack pointer in the 8051 is only 8 bits wide, which means that it can take value 00 to FFH. When 8051 powered up, the SP register contains value 07.
7FH
30H
2FH
20H
1FH
17H
10H
0FH
07H
08H
18H
00H
Register Bank 0
(Stack) Register Bank 1
Register Bank 2
Register Bank 3
Bit-Addressable RAM
Scratch pad RAM

## Slide 32: On-Chip Memory Internal RAM

## Slide 33: Registers
07
06
05
04
03
02
01
00
R7
R6
R5
R4
R3
R2
R1
R0
0F
08
17
10
1F
18
Bank 3
Bank 2
Bank 1
Bank 0
Four Register Banks
Each bank has R0-R7
Selectable by psw.2,3

## Slide 37: Register Banks
Active bank selected by PSW [RS1,RS0] bit
Permits fast “context switching” in interrupt service routines (ISR).

## Slide 38: Bit Addressable Memory
20h – 2Fh (16 locations X 8-bits = 128 bits)
7F |  |  |  |  |  |  | 78
 |  |  |  |  | 1A |  | 
 |  |  |  |  |  |  | 10
0F |  |  |  |  |  |  | 08
07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
27
26
25
24
23
22
21
20
2F
2E
2D
2C
2B
2A
29
28
Bit addressing:
mov C, 1Ah
or
mov C, 23h.2

## Slide 39: Special Function Registers
DATA registers
CONTROL registers
  Timers
  Serial ports
  Interrupt system
  Analog to Digital converter
  Digital to Analog converter
  Etc.
Addresses 80h – FFh
Direct Addressing used to access SPRs

## Slide 40
SFR Memory:

## Slide 41
Addresses of Registers :

## Slide 42: Programming model

## Slide 43: 8051 Programming Model