## Slide 1
8051- Interrupts

## Slide 2: 8051- Interrupts
An interrupt is an external or internal event that interrupts the μc to inform it that a device needs its service.
A single microcontroller can serve several devices by two ways
1. Interrupts 2. Polling
1. Interrupt
Whenever any device needs its service, the device notifies the microcontroller by sending it an interrupt signal
Upon receiving an interrupt signal, the microcontroller interrupts whatever it is doing and serves the device
The program which is associated with the interrupt is called the interrupt service routine (ISR) or interrupt handler
2. Polling
The microcontroller continuously monitors the status of a given device
When the conditions met, it performs the service
It is not efficient, since it wastes much of the μc’s time by polling devices that do not need service

## Slide 3: 8051- Interrupts
It finishes the instruction it is executing and saves the address of the next instruction (PC) on the stack.
2. It also saves the current status of all the interrupts internally
3. The microcontroller gets the address of the ISR from the interrupt vector table and jumps to it. It starts to execute the interrupt service subroutine until it reaches the last instruction of the subroutine which is RETI (return from interrupt).
4. Upon executing the RETI instruction, the microcontroller returns to the place where it was interrupted. First, it gets the program counter (PC) address from the stack & then it starts to execute from that address.
Sequence of steps involved in how 8051 services an interrupt

## Slide 4: 8051- Interrupts
8051 has 6 Interrupts.
  RESET : power up reset : Non Maskable
  External Interrupts : 2  INT 0, INT 1
  Internal Interrupts : 3  Timer: TF 0, TF1; Serial COM ( RI or TI)

## Slide 5: 8051- Interrupts
8051 has two interrupt related registers;
1. Interrupt Enable Register : IE
2. Interrupt Priority Register : IP (Bit Addressable)

## Slide 6
1. Interrupt Enable Register : IE
8051- Interrupts

## Slide 7
Example : Show the instructions to
(a) enable the serial interrupt, timer 0 interrupt, and external hardware interrupt 1 (EX1),and
(b) disable (mask) the timer 0 interrupt, then
(c) show how to disable all the interrupts with a single instruction.
Solution:
(a) MOV IE, #10010110B ;enable serial, ;timer 0, EX1
Another way to perform the same manipulation is
SETB IE.7 ;EA=1, global enable
SETB IE.4 ;enable serial interrupt
SETB IE.1 ;enable Timer 0 interrupt
SETB IE.2 ;enable EX1
(b) CLR IE.1 ; mask (disable) timer 0 ;interrupt only
(c) CLR IE.7 ; disable all interrupts
8051- Interrupts
EA |  |  | ES | ET1 | EX1 | ET0 | EX0
IE.7 | IE.6 | IE.5 | IE.4 | IE.3 | IE.2 | IE.1 | IE.0

## Slide 8
8051- Interrupts
By default

## Slide 9
8051- Interrupts