## Slide 1: Memory Segmentation of Intel 8086

## Slide 2: Memory Segmentation
The total memory size is divided into segments of various sizes.
A segment is just an area in memory.
The process of dividing memory is called Segmentation.

## Slide 3: Memory Segmentation
In memory, data is stored as bytes.
Each byte has a specific address.
Intel 8086 has 20 lines address bus.
With 20 address lines, the memory that can be addressed is 220 bytes.
220 = 1,048,576 bytes (1 MB).
8086 can access memory with address ranging from 00000 H to FFFFF H.

## Slide 4: Memory Segmentation
In 8086, memory has four different types of segments.
These are:
  Code Segment
  Data Segment
  Stack Segment
  Extra Segment

## Slide 5: Segment Registers
Each of these segments are addressed by an address stored in corresponding segment register.
These registers are 16-bit in size.
Each register stores the base address (starting address) of the corresponding segment.
Because the segment registers cannot store 20 bits, they only store the upper 16 bits.

## Slide 6: Segment Registers

## Slide 7: Segment Registers
How is a 20-bit address obtained if there are only 16-bit registers?
The answer lies in the next few slides.
The 20-bit address of a byte is called its Physical Address.
But, it is specified as a Logical Address.
Logical address is in the form of:
  Base Address : Offset
Offset is the displacement of the memory location from the starting location of the segment.

## Slide 8: Example
The value of Data Segment Register (DS) is 2222 H.
To convert this 16-bit address into 20-bit, the BIU appends 0H to the LSBs of the address.
After appending, the starting address of the Data Segment becomes 22220H.

## Slide 9: Example (Contd.)
If the data at any location has a logical address specified as:
  2222 H : 0016 H
Then, the number 0016 H is the offset.
2222 H is the value of DS.

## Slide 10: Example (Contd.)
To calculate the effective address of the memory, BIU uses the following formula:
  Effective Address = Starting Address of Segment + Offset
To find the starting address of the segment, BIU appends the contents of Segment Register with 0H.
Then, it adds offset to it.

## Slide 11: Example (Contd.)
Therefore:
EA = 22220 H
+ 0016 H
------------
22236 H

## Slide 12: Example (Contd.)
BYTE – 0
BYTE – 1
BYTE – 2
- - - - -
Addressed Byte
2222 H
DS Register
22220 H
Offset = 0016 H
22236 H

## Slide 13: Max. Size of Segment
All offsets are limited to 16-bits.
It means that the maximum size possible for segment is 216 = 65,535 bytes (64 KB).
The offset of the first location within the segment is 0000 H.
The offset of the last location in the segment is FFFF H.

## Slide 14: Where to Look for the Offset
Segment | Offset Registers | Function
CS | IP | Address of the next instruction
DS | BX, DI, SI | Address of data
SS | SP, BP | Address in the stack
ES | BX, DI, SI | Address of destination data (for string operations)

## Slide 15: Question
The contents of the following registers are:
  CS = 1111 H
  DS = 3333 H
  SS = 2526 H
  IP = 1232 H
  SP = 1100 H
  DI = 0020 H
Calculate the corresponding physical addresses for the address bytes in CS, DS and SS.

## Slide 16: Solution
1. CS = 1111 H
The base address of the code segment is 11110 H.
Effective address of memory is given by 11110H + 1232H = 12342H.
2. DS = 3333 H
The base address of the data segment is 33330 H.
Effective address of memory is given by 33330H + 0020H = 33350H.
3. SS = 2526 H
The base address of the stack segment is 25260 H.
Effective address of memory is given by 25260H + 1100H = 26350H.

## Slide 17
Thank You
Have a Nice Day