## Slide 2: Data Transfer Instructions
MOV dest, source dest  source
Stack instructions
  PUSH byte ;increment stack pointer, ;move byte on stack
  POP byte ;move from stack to byte, ;decrement stack pointer
Exchange instructions
  XCH a, byte ;exchange accumulator and byte
  XCHD a, byte ;exchange low nibbles of ;accumulator and byte

## Slide 7: Exchange Instructions
two way data transfer
  XCH a, 30h ; a  M[30]
  XCH a, R0 ; a  R0
  XCH a, @R0 ; a  M[R0]
  XCHD a, R0 ; exchange “digit”
R0[7..4] R0[3..0]
a[7..4] a[3..0]
Only 4 bits exchanged

## Slide 8: Bit-Oriented Data Transfer
transfers between individual bits.
Carry flag (C) (bit 7 in the PSW) is used as a single-bit accumulator
RAM bits in addresses 20-2F are bit addressable
mov C, P0.0
mov C, 67h
mov C, 2ch.7

## Slide 9: SFRs that are Bit Addressable
SFRs with addresses ending in 0 or 8 are bit-addressable.
  (80, 88, 90, 98, etc)
Notice that all 4 parallel I/O ports are bit addressable.

## Slide 11: Arithmetic instructions

## Slide 12: Arithmetic Instructions
Mnemonic | Description
ADD A, byte | add A to byte, put result in A
ADDC A, byte | add with carry
SUBB A, byte | subtract with borrow
INC A | increment A
INC byte | increment byte in memory
INC DPTR | increment data pointer
DEC A | decrement accumulator
DEC byte | decrement byte
MUL AB | multiply accumulator by b register
DIV AB | divide accumulator by b register
DA A | decimal adjust the accumulator

## Slide 24: LOGICAL operators

## Slide 33: Rotate and Multiplication/Division
Note that a shift left is the same as multiplying by 2, shift right is divide by 2
  mov a, #3 ; A 00000011 (3)
  clr C ; C 0
  rlc a ; A 00000110 (6)
  rlc a ; A 00001100 (12)
  rrc a ; A 00000110 (6)

## Slide 42: Program Flow Control instructions